| GNL-1880xx (7.62x7.62) PIRANHA TYPE Flux LED Lamp ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 40 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 180 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-1880UEC AlGaInP Orange Red Water Clear 625 2.0 350 450 70° GNL-1880URC GaAlAs Pure Red Water Clear 660 1.9 250 350 70° GNL-1880UYC AlGaInP Yellow Water Clear 590 2.0 350 450 70° GNL-1880UEC-TL AlGaInP Orange Red Water Clear 625 2.0 800 1000 70° GNL-1880UYC-TL AlGaInP Yellow Water Clear 590 2.0 1100 1300 70° GNL-1880UYOC-TL AlGaInP Amber Water Clear 610 2.0 1100 1300 70° GNL-1880UBC InGaN Blue Water Clear 470 3.5 600 800 70° GNL-1880BGC InGaN Cyan Water Clear 505 3.5 700 900 70° GNL-1880PGC InGaN Pure Green Water Clear 525 3.5 1400 1800 70° GNL-1880UBC-TL InGaN Blue Water Clear 470 3.5 800 900 70° GNL-1880BGC-TL InGaN Cyan Water Clear 505 3.5 900 1100 70° GNL-1880PGC-TL InGaN Pure Green Water Clear 525 3.5 3000 4000 70° GNL-1880UWC InGaN Ultra White Water Clear 5500K-7000K 3.5 800 1200 70° GNL-1880UWC-15C InGaN Ultra White Water Clear 5500K-7000K 3.5 1700 1900 70° GNL-1880UWC-TL-15C InGaN Ultra White Water Clear 5500K-7000K 3.5 4000 5000 90° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.