| GNL-3015xx (Φ3mm ROUND TYPE) Bi-color series ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip Temperature (5 seconds,1.6mm from body ) 300 ±5 ℃ |  |
| --- | --- |
| Part Number EMITTED COLOR Mix Emitted Color Lens Color Peak Wave length (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-3015EGW GaAsp/Gap Hi-Eff Red Orange White Diffused 635 2.0 8.0 15 60° Gap Green 565 2.1 5.0 10 GNL-3015YGW Gap Green Yellow-Green White Diffused 565 2.1 5.0 10 60° GaAsp Yellow 585 2.1 5.0 10 GNL-3015UEUBW AlGaInP Super Red Purple White Diffused 625 2.0 120 200 60° InGaN Super Blue 470 3.5 110 180 GNL-3015UEUGW AlGaInP Super Red Orange White Diffused 625 2.0 120 200 60° AlGaInP Super Green 572 2.0 100 150 GNL-3015EGC GaAsp/Gap Hi-Eff Red Orange Water Clear 635 2.0 20 40 30° Gap Green 565 2.1 15 25 GNL-3015UYUGC AlGaInP Super yellow Yellow-Green Water Clear 590 2.1 270 500 30° AlGaInP Super Green 572 2.1 260 500 GNL-3015UEUGC AlGaInP Super Red Orange Water Clear 625 2.0 280 500 30° AlGaInP Super Green 572 2.0 260 350 GNL-3015UEUBC AlGaInP Super Red Purple Water Clear 625 2.0 280 500 30° InGaN Super Blue 470 3.5 350 450 |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.